## Slide 1: Deriving Use Cases from System Requirements
Initiating actors (“users”) are already identified in user stories
Participating actors identified as part of use case analysis
REQ1: Keep door locked and auto-lock REQ2: Lock when “LOCK” pressed REQ3: Unlock when valid key provided
REQ4: Allow mistakes but prevent dictionary attacks REQ5: Maintain a history log
REQ6: Adding/removing users at runtime
REQ7: Configuring the device activation preferences
REQ8: Inspecting the access history REQ9: Filing inquiries
1
2
3
4
5
X Y
Initiator | Initiator’s Goal | Participants | Use Case Name
Tenant | Unlock and enter home. | Lock, Household Devices, Database, Bluetooth module | Unlock (UC-1)
Tenant | Lock the door. | Lock, Household Devices, Database | Lock (UC-2)
Landlord | Create a new user account and allow access to home. | Tenant, Database | AddUser (UC-3)
Landlord | Retire an existing user account and disable access. | Database | RetireUser (UC-4)
Tenant | Review the history of home accesses. | Database | ViewHistory (UC-5)
Tenant | Configure the operational preferences for household devices. | Database | SetDevicePrefs (UC-6)
Visitor | Visit a resident’s home. | Lock, Database | VisitHome (UC-7)

## Slide 2: Use Case 1: Unlock
Use Case UC-1:
Unlock
REQ1, REQ3, REQ4, and REQ5 stated in Table 2-1
Any of: Tenant, Landlord
To disarm the lock and enter, and get space lighted up automatically.
Related Requirem’ts:
Initiating Actor:
Actor’s Goal:
Participating Actors:
Preconditions:
Postconditions:
LockDevice, LightSwitch, Timer, Bluetooth module
The MAC address of bluetooth in the system database is non-empty.
The system displays the menu of available functions; at the door keypad the menu choices are “Lock” and “Unlock.”
Flow of Events for Main Success Scenario:
 1. Tenant/Landlord arrives at the door and selects the menu item “Unlock”
2. include::AuthenticateUser (UC-7)
<- 3. System (a) signals to the Tenant/Landlord the lock status, e.g., “disarmed,” (b) signals to LockDevice to disarm the lock, and (c) signals to LightSwitch to turn the light on
<- 4. System signals to the Timer to start the auto-lock timer countdown
 5. Tenant/Landlord opens the door, enters the home [and shuts the door and locks]
The auto-lock timer has started countdown from autoLockInterval.

## Slide 3: Use Case 4:Retire Uesr
Use Case UC-4:
Retire Uesr
REQ6 stated in Table 2-1
Landlord
To Remove tenant’s access
Database, Landlord
Related Requirements:
Initiating Actor:
Actor’s Goal:
Participating Actors:
Preconditions: Postconditions:
The MAC address of bluetooth must have been already in the database
Flow of Events for Main Success Scenario:
none
1.The landlord accesses the center of system.
2.The landlord can watch all the MAC address of Bluetooth which are in the database.
3. Then the landlord can remove some MAC address from the database.
4.After the operation, those tenants can’t unlock the lock unless their mobile phones’ MAC address of Bluetooth be added to the database again by the landlord.

## Slide 4: Acceptance Test Case for UC-1 Unlock
Test-case Identifier: TC-1 Use Case Tested: UC-1, main success scenario, and UC-7 Pass/fail Criteria: The MAC address of Bluetooth must have been already in the database. And then they open the Bluetooth function. If Bluetooth module in electronic lock senses that the mobile phone is within five meters, the door will be open. Otherwise, unlocking fails Input Data: Bluetooth module, door identifier | 
Test Procedure: | Expected Result:
Step 1. Use the phone whose MAC address of Bluetooth is not in the database. Step 2. Use the phone whose MAC address of Bluetooth is in the database out of 5 meters. Step 3. Use the phone whose MAC address of Bluetooth is in the database within 5 meters. | All the mobile phone can open the door. The electronic lock can’t distinguish the Bluetooth of the mobile.

## Slide 5: Acceptance Test Case for UC-4 Retire Uesr
Test-case Identifier: TC-4 Use Case Tested: main success scenario and UC-4 Pass/fail Criteria: The landlord can remove any MAC address of Bluetooth if he wants. And after operation those mobiles can’t unlock the door anymore. | 
Test Procedure: | Expected Result:
Step 1. The landlord watch the database. Step 2. Remove MAC address of Bluetooth as his wish. Step 3. Check the MAC address is still in the database or not Step 4. Check the phone whose MAC address of Blue tooth is not in the database can unlock the door or not. | 1.The landlord can’t watch all the MAC address. 2.The landlord can’t remove the MAC address successfully. 3.After the removing, the mobile can still open the door.